## Slide 1: Interrupts in Arduino

## Slide 2: Interrupts
As the name suggests, interrupts are routines that interrupt the normal code flow.
An interrupt routine contains a piece of code that the microcontroller on your board should execute whenever an event occurs.
Take the air-conditioner example.
Suppose it has the following temperature control settings: Switch off cooling whenever temperature reaches 18 degrees C. Now, there will be a temperature sensor that keeps measuring the temperature. Whenever it reports a temperature of 18 degrees Celsius, the normal code running on the AC microcontroller is interrupted, it executes the code to turn off cooling, and then the normal code resumes.

## Slide 3: When do interrupts get triggered?
There are various ways of triggering interrupts.
You can have an interrupt triggered when a button is pressed (basically when there is change in state of a pin from HIGH to LOW or LOW to HIGH).
You can have timer-based interrupts, which get triggered at regular intervals, you can have an interrupt when data is received via UART, or SPI, or Wire(I2C), and so on.

## Slide 4: Interrupt Service Routine
The code that gets executed whenever an interrupt even occurs, is stored inside a special kind of function called as the Interrupt Service Routine.
They have the following limitations −
They should not take in any parameters/ arguments
They cannot return anything
If there are multiple interrupts in your code, each having its own Interrupt Service Routine (ISR), then only one ISR can run at a time
If you wish to change the value of a variable within an ISR, you need to declare the variable as volatile.

## Slide 5: Types of Interrupt
There are two types of interrupts:
Hardware Interrupt: It happens when an external event occurs like an external interrupt pin changes its state from LOW to HIGH or HIGH to LOW.
Software Interrupt: It happens according to the instruction from the software. For example Timer interrupts are software interrupt.

## Slide 6: External Interrupt Pin Change Interrupt
•These interrupt are interpreted by hardware and are very fast.
• These interrupts can be set to trigger on the event of RISING or FALLING or LOW levels.
Arduinos can have more interrupt pins enabled by using pin change interrupts.
In ATmega168/328 based Arduino boards any pins or all the 20 signal pins can be used as interrupt pins.
They can also be triggered using RISING or FALLING edges.

## Slide 7: Using Interrupt in Arduino
In order to use interrupts in Arduino the following concepts are need to be understood.
•Interrupt Service Routine (ISR): Interrupt Service Routine or an Interrupt handler is an event that has small set of instructions in it. When an external interrupt occurs, the processor first executes these code that is present in ISR and returns back to state where it left the normal execution.
•ISR has following syntax in Arduino:

## Slide 8: Continued…
•digitalPinToInterrupt(pin): In Arduino Uno, NANO the pins used for interrupt are 2,3 & in mega 2,3,18,19,20,21. Specify the input pin that is used for external interrupt here.
•ISR: It is a function that is called when an external interrupt is done.
•Mode: Type of transition to trigger on, e.g. falling, rising, etc.
RISING: To trigger an interrupt when the pin transits from LOW to HIGH.
FALLING: To trigger an interrupt when the pin transits from HIGH to LOW.
CHANGE: To trigger an interrupt when the pin transits from LOW to HIGH or HIGH to LOW (i.e., when the pin state changes ).
•Some Conditions while using Interrupt
Interrupt Service Routine function (ISR) must be as short as possible.
Delay () function doesn’t work inside ISR and should be avoided.

## Slide 9: Continued…
const int buttonPin = 3;
void setup() {
// Initialize serial communication for debugging
Serial.begin(9600);
// Configure external interrupt 1 (INT1)
attachInterrupt(digitalPinToInterrupt(3), interruptFunction, RISING);
// Set the button pin as INPUT
pinMode(buttonPin, INPUT);
}
void loop() {
// Main loop code
// This loop can perform other tasks while waiting for the interrupt
}
void interruptFunction() {
// Code to be executed when external interrupt 1 (INT1) occurs
Serial.println("Interrupt occurred!");
// Additional processing, if needed
}
Example: The following example assumes a push button is connected to pin 3, and the interrupt will be triggered on the rising edge.

## Slide 10: Thank You!