## Slide 1: Tutorial
Implementation of itoa, atoi
3
Output Analysis
2
Difference between ‘strcpy’ and ‘strncpy’
1

## Slide 2
void setup() {
Serial.begin(9600);
const char source[] = "Hello, World!";
char destination[20];
strncpy(destination, source, 10);
destination[10] = '\0';
Serial.print("Source: ");
Serial.println(source);
Serial.print("Destination: ");
Serial.println(destination);
}
void loop() {
// Nothing to do in the loop
}
void setup() {
char source[] = "Hello, World!";
char destination[20];
strcpy(destination, source);
Serial.begin(9600);
Serial.print("Source: ");
Serial.println(source);
Serial.print("Destination: ");
Serial.println(destination);
}
void loop() {
// Nothing to do in the loop
}
Example of strncpy
Example of strcpy

## Slide 3
void setup() {
Serial.begin(9600);
}
void loop() {
char str1[] = "apple";
char str2[] = "apple";
char str3[] = "banana";
int result1 = strcmp(str1, str2);
int result2 = strcmp(str1, str3);
int result3 = strcmp(str3, str1);
Serial.print("Comparison between str1 and str2: ");
if (result1 < 0) {
Serial.println("str1 is less than str2");
} else if (result1 > 0) {
Serial.println("str1 is greater than str2");
} else {
Serial.println("str1 is equal to str2");
}
Serial.print("Comparison between str1 and str3: ");
if (result2 < 0) {
Serial.println("str1 is less than str3");
} else if (result2 > 0) {
Serial.println("str1 is greater than str3");
} else {
Serial.println("str1 is equal to str3");
}
Serial.print("Comparison between str3 and str1: ");
if (result3 < 0) {
Serial.println("str3 is less than str1");
} else if (result3 > 0) {
Serial.println("str3 is greater than str1");
} else {
Serial.println("str3 is equal to str1");
}
delay(1000); // Delay for 1 second before the next iteration
}

## Slide 4
int buttonPin = 2;
int switchPin = 3;
int ledPin = 11;
void setup() {
Serial.begin(9600);
pinMode(buttonPin, INPUT);
pinMode(switchPin, INPUT);
pinMode(ledPin, OUTPUT);
}
void loop() {
int buttonState = digitalRead(buttonPin);
int switchState = digitalRead(switchPin);
bool bothPressed = (buttonState == LOW && switchState == LOW);
if (bothPressed) {
digitalWrite(ledPin, HIGH);
Serial.println("Both button and switch are pressed.");
} else {
digitalWrite(ledPin, LOW);
}
bool eitherPressed = (buttonState == LOW || switchState == LOW);
if (eitherPressed) {
Serial.println("Either button or switch is pressed.");
}
}

## Slide 5
void setup() {
Serial.begin(9600);
char string[] = "12345";
int number = atoi(string);
int remainder = 0;
int reverseNumber = 0;
while (number != 0) {
remainder = number % 10;
reverseNumber = reverseNumber * 10 + remainder;
number = number / 10;
}
Serial.print("Integer number: ");
Serial.println(reverseNumber);
char stringName[6];
itoa(reverseNumber, stringName, 10);
Serial.print("Reversed Number as String: ");
Serial.println(stringName);
int checkName=strcmp(number, reverseNumber);
if (checkName==0){
Serial.println(“This is a palindrome number”);
}
else {
Serial.println(“this is not a palindrome number”);
}
}
void loop() {
// Nothing to do in the loop
}